## Slide 1: Big and Little Endian
Microprocessor architectures commonly use two different methods to store the individual bytes of multi byte numerical data in memory. This difference is referred to as “byte ordering” or “endian nature
Byte ordering: It is described the order in which a sequence of bytes are stored in computer memory.
Little and Big Endian
Intel x86 processors store a two-byte integer with the least significant byte first, followed by the most significant byte. This is called little-endian byte ordering
Other CPUs, such as the PowerPC CPU, store a two-byte integer with its most significant byte first, followed by its least significant byte. This is called big-endian byte ordering.

## Slide 2: x86 Data Types
The term endian refers to the way that multi-byte binary numbers are stored. For example, two-byte binary numbers can be stored in big-endian format (MSB LSB) or in little-endian format (LSB MSB).
APPLICATIONS:
Pentium (x86),VAX(virtual Addressing eXtension) are little-endian
IBM 370, Motorola 680x0 (Mac), and most RISC are big-endian
Internet is big-endian (Unix)
Notes: 15

## Slide 3: Endian Types
Big endian and little endian
Example: big-endian computer, the two bytes required for the hexadecimal number 4F52 would be stored as 4F52 in storage (if 4F is stored at storage address 1000, and, 52 will be at address 1001).
little-endian system, it would be stored as 524F (52 at address 1000, 4F at 1001).
Byte 4F52 | Memory address
4F (MSB) | 1000
52 (LSB) | 1001
Byte 524F | Memory address
52 | 1000
4F | 1001
Big Endian
Little Endian

## Slide 4: Byte Order (example) 78 56 34 12 (byte number)
Address Value (1) Value(2)
184(lowest add) 12 78
185 34 56
186 56 34
186(highest add) 78 12
i.e. read top down or bottom up?
Big-E
Little-E
LSB
Notes: 28