## Slide 1: CST8101 Computer Essentials
Microprocessor

## Slide 2: Microprocessor
Central Processing Unit (CPU)
Can perform millions of mathematical operations per second
Responsible for most of the data processing performed by the computer
Often referred to as the brains of the computer

## Slide 3: CPU

## Slide 4: Microprocessor
Clock
  The clock speed or clock rate is the speed at which the microprocessor executes instructions
  It is the maximum speed, not the speed at which it always runs
  This internal clock is used to regulate the rate at which instructions are executed and to synchronize all the various computer components
  The CPU requires a fixed number of clock cycles to execute each instruction
  Every instruction requires at least two clock cycles
Notes: bb

## Slide 5: Microprocessor
Front Side Bus or FSB
  Communication device between the CPU and the Northbridge and Southbridge (device such as RAM, Expansion Slots, HD)
  Communication is bi-directional
Back Side Bus
  Connects the CPU to the L2 and L3 Cache
    Faster than the FSB

## Slide 6: Microprocessor
FSB and BSB have since been replaced with QPI
QuickPath Interconnect or QPI
  Allows direct communication between the CPU and/or RAM, Expansion Slots, HD simultaneously.
  Communication is bi-directional
  Much Faster than FSB

## Slide 7: Quick Path Interconnect
Organized very similarly to the OSI model
  Physical layer
    The actual circuits connecting devices.
  Link layer
    Implements flow control.
  Routing layer
    The routing layer sends a 72-bit unit consisting of an 8-bit header and a 64-bit payload.

## Slide 8: Simple CPU – The Z80
Control Unit
Registers
Arithmetic Logic Unit
Bus Interfaces

## Slide 9: CPU Components Z-80
Execution (Control) Unit
  Decodes instructions
  Makes logical decisions
Arithmetic Logic Unit
  Performs integral calculations
  Performs comparisons
Registers
  Temporary storage spaces
  Known as general purpose registers: AX, BX, CX, DX
  NOT memory addresses
  Used for data manipulation by the CPU
Bus Interfaces
  Physical connections between CPU and three-bus architecture

## Slide 10: Arithmetic Logic Unit
Equal-to condition. In a test for this condition, the arithmetic/logic unit compares two values to determine if they are equal.
Less-than condition. To test for this condition, the computer compares values to determine if one is less than another.
Greater-than condition. In this type of comparison, the computer determines if one value is greater than another.
A computer can simultaneously test for more than one condition. In fact, a logic unit can usually discern six logical relationships: equal to, less than, greater than, less than or equal to, greater than or equal to, and not equal.

## Slide 11: Registers
Computers usually assign special roles to certain registers, including these registers:
An accumulator, which collects the result of computations.
An address register, which keeps track of where a given instruction or piece of data is stored in memory. Each storage location in memory is identified by an address, just as each house on a street has an address.
A storage register, which temporarily holds data taken from or about to be sent to memory.
A general-purpose register, which is used for several functions.

## Slide 12: Microprocessor
Three-Bus architecture
  Allows the CPU to specific type, size and location of data transfer
  Control bus
    Identifies whether the CPU is reading or writing data
  Address bus
    Identifies the location of where the data is being read/written
  Data bus
    Actual information being sent/received by the CPU

## Slide 13: Block diagram of Intel 900 series processor die image from Intel

## Slide 14: CPU Execution Cycle
The CPU executes every program one instruction at a time
Typically instructions are very simple, for example
  MOV
    Copy data to/from memory
  CMP
    Compare two values
  ADD
    Add two numbers together
  JMP
    Set the Program Counter to a new address
  Etc.

## Slide 15: CPU Execution Cycle
Each CPU instruction must experience three phases
  FETCH
    Data is read from memory, and transferred to CPU’s control unit
  DECODE
    CPU determines what is required to perform the instruction
  EXECUTE
    CPU performs the instruction

## Slide 16: CPU Execution Cycle
For complex instruction sets, this cycle can be quite costly in terms of time
Numerous optimizations have been developed to speed the process along
Such as …
  Wider Busses
  Pipelining
  Superscalar Architectures
  Branch Predictor
  Cache memory

## Slide 17: Performance Enhancements
Wider Data Busses
  Simply increased the number of wires connecting the CPU
  Data bus width has grown from 8 bits (Intel 8088) to 64 bits (for Dual Channel DDR)
  Allows more data to be carried simultaneously between CPU and memory
  Similar to more lanes on a highway

## Slide 18: Pipelining
All CPUs have a pipeline that the CPU uses to process a command
With a single pipeline all commands. Simple or complex, run through the same linear pipeline
Dual pipeline
  Dual pipelining allows two instructions to be processed at the same time
  The first pipeline, named U is the primary
  The second pipeline, named V can handle simple commands such as integer addition

## Slide 19: Pipelining
Quad pipelining
  Able to handle four separate pipelines simultaneously
  On average, this enabled the equivalent of three simultaneous processes
Dynamic processing
  Some time consuming actions could cause the CPU to wait up to 10 to 20 clock cycles
  When the CPU was forced to wait, it took advantage of the wait to look at the pipeline to see if any other commands where complete
  Pentium IV allowed a pipeline depth of 20 stages or more

## Slide 20: Pipelining
Pipeline stages
  Each stage allows a portion of instruction decode and execution to occur
  Typical stages include
    instruction fetch
    instruction decode
    memory read
    ALU operation
    memory write

## Slide 21: Pipelining Illustrated
The advantages of pipelining
Non Pipelined Pipelined
Single Instruction Multiple Instructions

## Slide 22: Performance Enhancements
Superscalar Architectures
  If one pipeline is good …
  Multiple pipelines may be better!
  Superscalar implements multiple CPU pipelines
  Permits multiple instructions to be executed simultaneously

## Slide 23: Branch Predictor
Originally found on high-end mainframe processors
Requirement for efficiently using a deep pipeline
By default, programs execute sequentially .. Instructions executed in the same order as they appear in memory

## Slide 24: Branch Predictor
Branch Prediction Unit (BPU) permits CPU to anticipate where the next program branch will come from
Processor is able to keep instruction pipeline full at high speeds
Part of Intel’s Advance Dynamic Execution (ADE) engine – component in Pentium IV design

## Slide 25: Cache Memory
Cache allows CPU very quick temporary storage for often-used data
Similar to a high-speed buffer only more intelligent
To cache means to set aside data used in the past in a fast storage area
When the CPU needs that data again is can easily and quickly access the data

## Slide 26: Cache Memory
How caching works:
  The cache controller anticipates what data will be required next
  Intel states that their processors are correct around 90% of the time
Three levels of processor cache exist in modern computers
  Level 1
  Level 2
  Level 3

## Slide 27: Cache Memory
Level 1 (L1) Cache
  Originated with the 486 family of processors
  Ranges from 8 KB to 64KB
  Integrated into the CPU
  Runs at the full core speed of the CPU
  Processors always run faster than the data bus

## Slide 28: Cache Memory
Level 2 (L2) Cache
  Up to 1 MB of storage
  Originally ran slower than L1 cache
  Now CPU resident for Pentium class and running at the processor speed
  Acts as secondary buffer between system memory and CPU

## Slide 29: Cache Memory
Level 3 (L3) Cache
  Resides on the CPU
    Older AMD/Intel CPU’s have L3 cache residing on the motherboard
  Size of the Cache on Processors range from 512 KB to 8 MB

## Slide 30: Multimedia Instructions Sets
MMX
  Acronym - does not stand for anything
  Circuit in the CPU that is used to speed up the execution of multimedia code such as graphics and sound
  Performs a single instruction on multiple data – often called a SIMD

## Slide 31: Multimedia Instructions
SSE
  70 new instructions were added to MMX to speed up processing in 1999
SSE2
  144 new instructions
SSE3
  13 new instructions – released in with the Prescott Pentium 4

## Slide 32: Other Performance Factors
Performance factors include
  CPU clock speed
  CPU bus speed
  Chipset
  RAM type and amount
  Etc, etc
The only thing that’s constant in technology, is change!

## Slide 33: Microprocessor Comparison
Comparison chart for Intel processors
Name | Date | Transistors | Microns | Clock Speed | Data Width | MIPS
8080 | 1974 | 6,000 | 6 | 2 MHz | 8 bits | 0.64
8088 | 1979 | 29,000 | 3 | 5 MHz | 16 bits 8-bit bus | 0.33
80286 | 1982 | 134,000 | 1.5 | 6 MHz | 16 bits | 1
80386 | 1985 | 275,000 | 1.5 | 16 MHz | 32 bits | 5
80486 | 1989 | 1,200,000 | 1 | 25 MHz | 32 bits | 20
Pentium | 1993 | 3,100,000 | 0.8 | 60 MHz | 32 bits 64-bit bus | 100
Pentium II | 1997 | 7,500,000 | 0.35 | 233 MHz | 32 bits 64-bit bus | ~300
Pentium III | 1999 | 9,500,000 | 0.25 | 450 MHz | 32 bits 64-bit bus | ~510
Pentium IV | 2000 | 42,000,000 | 0.18 | 1.5 GHz | 32 bits 64-bit bus | ~1,700

## Slide 34: About the Chart
Transistors
  The number of transistors on the chip
  Notice the number of transistors has steadily gone up
Microns
  The width, in micros, of the smallest wire on the chip
  A human hair is 100 microns thick

## Slide 35: About the Chart
Data Width
  Is the width of the ALU
  An 8-bit ALU can manipulate two 8 bit numbers
MIPS
  Is roughly the performance rating for the CPU
  Stands for “millions of instructions per second”

## Slide 36: Lecture Summary
Major CPU Components
  Control Unit, ALU, Busses
  FPU, Branch Predictor, Cache
Performance Factors
  Wider busses, pipelining, superscalar architecture, branch predictor, cache